(CodeName) MyUSB
© Dean Camera, 2007

API Documentation
PRELIMINARY – SUBJECT TO CHANGE

http://www.fourwalledcubicle.com
deam (at) fourwalledcubicle (dot) com

Document Contents:

1) Overview and Purpose

2) Directory Structure
Drivers Directory
USB1287 Directory
USBKEY Directory
USB Directory
LowLevel Directory
MidLevel Directory
HighLevel Directory

Common Directory

3) Library API
Drivers Directory
USB1287 Directory
ADC.h

USBKEY Directory
Bicolour.h
HWB.h
Joystick.h

USB Directory
LowLevel Directory
LowLevel.h
MidLevel Directory
MidLevel.h
USB.h

Common Directory
Atomic.h
FunctionAttributes.h
ISRMacro.h
Scheduler.h

1) Overview and Purpose

The primary purpose of the MyUSB library is to give an easy to use, open source, generously licensed USB driver for the USB-equipped Atmel AVR1287 microcontroller. The library also includes drivers for the various hardware components available on the AVR1287 demonstration board, the AT90SUSBKEY and also drivers for other low-level functionality of the 90S1287 AVR microcontroller.

This library was created to further my own knowledge of the AVR microcontrollers, and to gain experience with working with the USB interface. The AVR1287 microcontroller was chosen because it offers hardware USB support and is available on the ready-packaged USBKEY board.

Creating a USB driver for the USB-equipped AVRs is far more than just register twiddling; it requires drivers for the different layers of the USB specification (low, mid and high). The MyUSB library provides the low and mid level layers as well as general USB management, and exposes an API for use in the user-made high-level (device) layer.

The MyUSB library is licensed under the GPL license, version 2.

2) Directory Structure

The structure of the MyUSB library is designed to be straightforward and logical. The root of the library consists of two directories, Drivers and Common, which may contain other child directories for better organization of the library components.

Drivers Directory

This directory contains the hardware and software drivers for the MyUSB library. It contains subdirectories for the main aspects of the MyUSB library.

USB1287 Directory

This directory contains low-level drivers for the 90SUSB1287 AVR microcontroller, that are not related to USB functionality (which has its own directory).

USBKEY Directory

This directory contains the individual drivers for the hardware available on the Atmel USBKEY board. Each file pertains to one hardware aspect, and some files may take advantage of the functionality provided by others (for example, the Temperature Sensor driver makes use of the Analogue-to-Digital driver).

USB Directory

This directory contains the files required for USB operation, and is the heart of the MyUSB library. This directory contains master USB header files, as well as subdirectories for the two layers and high level routines provided by the library.

LowLevel Directory

This directory contains the low level USB management files, which manage the USB hardware at the lowest level (register manipulations).

MidLevel Directory

This directory contains the mid level USB management file, which manage the USB data endpoints.

HighLevel Directory

This directory contains the high level USB routines for managing connections and disconnections, etc.

Common Directory

This directory contains common source files which give functionality common to the entire library or to the end-application.

3) Library API

Each file in the library is listed in this section, detailing it's API interface.

Some library API entries are listed as functions despite being macros in the code; these are written so that they may be assumed to be inline functions, and behave as such.

USB1287 Directory

Name:	ADC.h
Purpose:	Analogue to Digital Driver for the USB1287
Location:	Drivers/USB1287/ADC.h
Requirements:	Drivers/USB1287/ADC.c (to be built with project)

Use:
#include “MyUSB/USB1287/ADC.h”

Macros:
None

Type Defines:
None

Functions:
void ADC_Init(void)
Configures and turns on the ADC subsystem, ready for a conversion. Must be called once at the start of the user program before any conversions take place.

void ADC_On(void)
Turns on the ADC subsystem.

void ADC_Off(void)
Turns off the ADC subsystem.

bool ADC_GetStatus(void)
Returns the status of the ADC subsystem (true if on, false if currently off).

void ADC_SetupChannel(uint8_t Channel)
Configures an ADC channel for ADC use. This routine will disable the digital portion of a given ADC channel (making it analogue-only and saving power) and will configure the pin as an input. This is required to be used once only before reading a channel.

uint16_t ADC_ReadChannel(uint8_t Channel)
Does a complete reading of the specified channel, returning the 10-bit result. Note that this uses spin-loops while waiting for the conversion to complete, and as such should not be used in time-critical sections of code.

void ADC_StartReading(uint8_t Channel)
Begins an ADC conversion for a specified channel. This will not wait for the conversion to complete, nor will it return a result. Should be used in conjunction with the ADC_IsReadingComplete() and ADC_GetReading() routines.

bool ADC_IsReadingComplete(void)
Returns zero whilst an ADC conversion is taking place. Should be used after a call to ADC_StartReading to monitor the conversion status.

uint16_t ADC_GetReading(void)
Returns the converted value of the last ADC conversion. Should be used after a true value of ADC_IsReadingComplete in order to retrieve the conversion result.

USBKEY Directory

Name:	Bicolour.h
Purpose:	Driver for the USBKEY onboard pair of Bicolour LEDs
Location:	Drivers/USBKEY/Bicolour.h
Requirements:	None

Use:
#include “MyUSB/USBKEY/Bicolour.h”

Macros:
BICOLOUR_LED1_RED
Red colour for the left-most Bicolour LED (with respect to the Joystick)

BICOLOUR_LED1_GREEN
Green colour for the left-most Bicolour LED (with respect to the Joystick)

BICOLOUR_LED1_ORANGE
Orange colour for the left-most Bicolour LED (with respect to the Joystick)

BICOLOUR_LED2_RED
Red colour for the right-most Bicolour LED (with respect to the Joystick)

BICOLOUR_LED2_GREEN
Green colour for the right-most Bicolour LED (with respect to the Joystick)

BICOLOUR_LED2_ORANGE
Orange colour for the right-most Bicolour LED (with respect to the Joystick)

BICOLOUR_ALL_LEDS
Orange colour for the both Bicolour LEDs of the USBKEY

Type Defines:
None

Functions:
void Bicolour_Init(void)
Configures the appropriate ports of the 90S1287 as outputs for controlling the Bicolour LEDs. This function must be called once at the start of a program, before any other Bicolour LED calls.

void Bicolour_TurnOnLeds(uint8_t LedMask)
Accepts a mask comprising of colours for both Bicolour LEDs, turning the passed LEDs on. This will have no effect on any LEDs that are already turned on.

void Bicolour_TurnOffLeds(uint8_t LedMask)
Accepts a mask comprising of colours for both Bicolour LEDs, turning the passed LEDs off. This will have no effect on any LEDs that are already turned off.

void Bicolour_SetLeds(uint8_t LedMask)
Accepts a mask comprising of colours for both Bicolour LEDs, changing both Bicolour LEDs to the exact colours specified. This will turn on and off the LEDs as appropriate in order to display the passed mask exactly as a LED pattern.

void Bicolour_SetLed(uint8_t LedNumber, uint8_t LedMask)
Turns the Bicolour LED specified by LedNumber (one or two) to the passed mask exactly (single-LED version of SetLeds).

uint8_t Bicolour_GetLeds(void)
Returns the mask of the current Bicolour LEDs state. With set values corresponding to lit LEDs.

Name:	HWB.h
Purpose:	Driver for the USBKEY onboard HWB button (located next to onboard reset button)
Location:	Drivers/USBKEY/HWB.h
Requirements:	None

Use:
#include “MyUSB/USBKEY/HWB.h”

Macros:
None

Type Defines:
None

Functions:
void HWB_Init(void)
Configures the appropriate port of the 90S1287 as an input with pullup for reading the position of the HWB hardware button. This function must be called once at the start of a program, before any calls to GetStatus.

bool HWB_GetStatus(void)
Returns the boolean status (true = pressed) of the HWB's current state.

Name:	Joystick.h
Purpose:	Driver for the USBKEY onboard joystick (located next to battery connector)
Location:	Drivers/USBKEY/Joystick.h
Requirements:	None

Use:
#include “MyUSB/USBKEY/Joystick.h”

Macros:
JOY_LEFT
Mask for GetStatus, which determines if the joystick is in the left position.
JOY_RIGHT
Mask for GetStatus, which determines if the joystick is in the right position.
JOY_UP
Mask for GetStatus, which determines if the joystick is in the up position.
JOY_DOWN
Mask for GetStatus, which determines if the joystick is in the down position.
JOY_PRESS
Mask for GetStatus, which determines if the joystick is in the depressed position.

Type Defines:
None

Functions:
void Joystick_Init(void)
Configures the appropriate ports of the 90S1287 as inputs with pullup for reading the position of the joystick hardware. This function must be called once at the start of a program, before any calls to GetStatus.

uint8_t Joystick_GetStatus(void)
Returns an eight-bit value containing flags for the various positions (should be masked off with the position macros defined above). Note that more than one position may be set at one time – for example, left and pressed, or up and right.

Name:	Temperature.h
Purpose:	Driver for the USBKEY onboard temperature sensor
Location:	Drivers/USBKEY/Temperature.h
Requirements:	Drivers/USBKEY/Temperature.c (to be built with project)

Use:
#include “MyUSB/USBKEY/Temperature.h”

Macros:
TEMP_ADC_CHANNEL
Channel value of the on-board temperature sensor. May be used to get the raw sensor ADC value via the routines exposed by the ADC header file, or to prepare the temperature sensor channel using the same library header..
TEMP_MIN_TEMP
Minimum reportable temperature of of GetTemperature routine. Temperatures below this will report as this value.
TEMP_MAX_TEMP
Maximum reportable temperature of of GetTemperature routine. Temperatures above this will report as this value.

Type Defines:
None

Functions:
int8_t Temperature_GetTemperature(void)
Returns the current temperature of the USBKEY, as reported by the onboard temperature sensor. Must be called after the Temperature Sensor ADC channel is initialized (see ADC.h documentation). Returned value is signed, and is between TEMP_MIN_TEMP and TEMP_MAX_TEMP, inclusive.

USB Directory

TO BE DOCUMENTED

Common Directory

Name:	Atomic.h
Purpose:	Atomic access library for AVRGCC
Location:	Common/Atomic.h
Requirements:	None

Use:
#include “MyUSB/Common/Atomic.h”

Macros:
ATOMIC_RESTORESTATE
Exit mode for ATOMIC_BLOCK. Block will save the current Global Interrupt status bit on entry, and will restore its value upon exiting the atomic block.
ATOMIC_FORCEON
Exit mode for ATOMIC_BLOCK. Block will turn off the Global Interrupt status bit on entry, and turn it back on upon exiting the atomic block. Use in sections where the Global Interrupt status bit is known to be set, to save space and time.
NONATOMIC_RESTORESTATE
Exit mode for NONATOMIC_BLOCK. Block will save the current Global Interrupt status bit on entry, and will restore its value upon exiting the non-atomic block.
NONATOMIC_FORCEOFF
Exit mode for NONATOMIC_BLOCK. Block will turn on the Global Interrupt status bit on entry, and turn it back off upon exiting the non-atomic block. Use in sections where the Global Interrupt status bit is known to be cleared, to save space and time.

Type Defines:
None

Functions:
void ATOMIC_BLOCK(uint8_t ExitMode)
Creates a block of code where atomic access of data is guaranteed; i.e. the Global Interrupt status bit is disabled to prevent interrupts from occurring during the block. An ATOMIC_BLOCK should occur nested within an existing function. The exit behavior of the block should be specified using the above defined macros. Exit behavior will occur automatically at any point that the block terminates. May be nested inside of a NONATOMIC_BLOCK.

void NONATOMIC_BLOCK(uint8_t ExitMode)
Creates a block of code where atomic access of data is not guaranteed; i.e. the Global Interrupt status bit is enabled to allow interrupts to occur during the block's execution. A NONATOMIC_BLOCK should occur nested within an existing function. The exit behavior of the block should be specified using the above defined macros. Exit behavior will occur automatically at any point that the block terminates. May be nested inside of an ATOMIC_BLOCK.

Name:	FunctionAttributes.h
Purpose:	Function attributes for AVRGCC functions
Location:	Common/FunctionAttributes.h
Requirements:	None

Use:
#include “MyUSB/Common/FunctionAttributes.h”

Macros:
ATTR_NO_RETURN
When applied to a function, this attribute indicates to the GCC compiler that a function will never return.
ATTR_INIT_SECTION(x)
When applied to a function, this attribute indicates to the GCC compiler that a function belongs in the initialization section specified as “x” - see GCC init. sections documentation.
ATTR_WARN_UNUSED_RESULT
Indicates that a function should give a warning if it's return value is ignored at the point of call.
ATTR_NON_NULL_PTR_ARGS(x)
Indicates that the argument “x” (1-based) is a pointer that should never be passed a NULL value.
ATTR_NAKED
Indicates that a function should have no generated prologue or epilogue code.

Type Defines:
None

Functions:
None

Name:	ISRMacro.h
Purpose:	ISR Macro for GCC ISRs
Location:	Common/ISRMacro.h
Requirements:	None

Use:
#include “MyUSB/Common/ISRMacro.h”

Macros:
BADISR_vect
Symbollic name for the default ISR vector, called when an untrapped interrupt occurs.
ISR_NOBLOCK
ISR attribute. Specifies a non-blocking ISR, i.e. an ISR where Global Interrupts are enabled during its execution, allowing for nested ISRs to occur.
ISR_BLOCK
ISR attribute. Specifies a blocking ISR, i.e. An ISR where Global Interrupts are disabled during its execution.
ISR_NAKED
ISR attribute. Specifies an ISR with no epilogue or prologue generated. User is responsible for pushing and poping all relevant data and registers.
ISR_ALIASOF(v)
ISR attribute, GCC versions 4.2 and above only. Aliases an ISR vector to the vector specified by “v”.
ISR_ALIAS_COMPAT(vector, aliasof)
Creates an ISR which is an alias to the vector specified by “aliasof”. Compatible with all versions of GCC, however the aliased vector will contain a jump (JMP) instruction that the non-aliased vector will not have.
ISR(vector, attributes)
Creates an ISR with the specified attributes that handles the vector indicated by “vector”. “Attributes” may be one or more of the above ISR attributes, separated by spaces.

Type Defines:
None

Functions:
None

Name:	Scheduler.h
Purpose:	Basic round-robbin scheduler
Location:	Common/Scheduler.h
Requirements:	Common/Scheduler.c(to be built with project)

Use:
#include “MyUSB/Common/Scheduler.h”

Macros:
TASK(name)
Defines a new task of the specified name, Tasks should be designed to be called multiple times; when a task is ready to yield to the next task, it should return.

The task (without accompanying body) should also be listed in the appropriate header file, to expose it to the scheduler.
TASK_LIST
Defines the list of tasks for the scheduler. Should occur once in the main C file only. TASK_LIST should contain an array of task names, identical to the names given to each task by the TASK macro.

Type Defines:
SchedulerDelayCounter_t
Type used by HasDelayElapsed to store the tick counter. Create a static SchedulerDelayCounter_t in your tasks before calling HasDelayElapsed with it to delay a number of ticks.

Functions:
void Scheduler_Start(void)
Starts the scheduler running. Each task in TASK_LIST is executed sequentially forever.

void Scheduler_IncrementElapsedDelay(void)
Increments the scheduler tick counter by one. Use to allow HasDelayElapsed to check for elapsed delays. By continuously incrementing the tick counter after a known delay, tasks can be delayed in execution until a specified delay has elapsed.

bool Scheduler_HasDelayElapsed(uint8_t Delay, SchedulerDelayCounter_t Count)
Checks to see if the specified tick delay has elapsed, by comparing the delta of the scheduler's main tick counter with the task delay counter (a static SchedulerDelayCounter_t that must be user-defined within a task) and returns true (and resets the task delay counter) if the specified delay (in ticks) has elapsed. Use to delay the execution of tasks by a known duration.